## Slide 1: COMP 558 Lecture 3 RGB Thurs. Sept. 6, 2018

## Slide 2: Cameras
Digital SLR (annual sales ~ 10 million units per year)
Smart phone (annual sales: over 1 billion units per year)

## Slide 3: Image size
1 megapixel (one million pixels)
e.g. “720p” is 1 MP (1280 x 720 pixels, ‘p’ for progressive)
“1080p” full high definition (HD) is 2 MP (~2K x 1K pixels)
“ultra HD” is 8 MP (about 4K x 2K)

## Slide 4: Pinhole Camera Model
(X, Y, Z )
3D scene point
position
(x, y)
2D image
pixel position
Here we ignore that cameras have lenses.

## Slide 5: Real Digital Camera (!)

## Slide 6: What is a digital image ?
Typically, 3 x 8 bits per pixel (RGB).
i.e. 3 values from 0 to 255
R channel
G channel
B channel

## Slide 7: RGB values: 0 to 255 (8 bits)
(255, 255, 255)
(255, 255, 0)
(255, 0, 255)
(0, 0, 255)
(0, 255, 255)
(0, 255, 0)
(0, 0, 0)
Red
(255, 0, 0)

## Slide 8
R channel
G channel
B channel

## Slide 9: Why RGB ?

## Slide 10: Why RGB ?
Human vision is trichromatic (Thomas Young ~1800)
The human eye has three types of color photoreceptors, called cones.
Cameras sensors are designed to mimic the spectral response of cones.

## Slide 11: Isaac Newton’s discovery of color spectra (1666)

## Slide 12
Light consists of electromagnetic waves from 400-700 nm.

## Slide 13: Light Spectrum
l
400 nm 700 nm
intensity

## Slide 14: Spectral sensitivity of three types of cones in eye (RGB sensors mimic this – next slide)
Fraction of light of wavelength l absorbed.
(Curves are normalized to 1 for illustration purposes,.)
R - long
G - medium
B - short

## Slide 15: Example: RGB spectral sensitivity for Canon camera These curves will differ between cameras. Yes, this is an issue.
http://astrosurf.com/buil/50d/test.htm
http://www.gujinwei.org/research/camspec/db.html

## Slide 16: Bayer Pattern
There are twice as many green subpixels as red & blue. The RGBG quadruples per pixel are spatially displaced.
Color filter array (CFA)
“Color blind” sensors
(CCD vs. CMOS technology: details omitted)

## Slide 17: Where do RGB values come from ?
For digital images, the RGB values represent measurements of light intensity.

## Slide 18: Linear Model
- spectrum of light arriving at pixel location
- spectral transmittance of color filter (R,G, or B)

## Slide 19
=
3 x 1 3 x N N x 1
The linear model describes how much light reaches a R,G, or B pixel.

## Slide 20: Exposure
The pixel value also depends on the duration of the measurement.
() = * t
where t is the exposure time.
However, this is not the RGB value.

## Slide 21: Analog-to-Digital conversion
The sensor measures the exposure signal at each R,G,B pixel.
(Mechanism: Photon is absorbed, releasing an electron )
This signal is then digitized : quantized and then coded in binary.
(Sometimes more than 8 bits per value at this stage.)

## Slide 22: Overexposed versus Underexposed images
https://photographylife.com/underexposure-and-overexposure-in-photography

## Slide 23: Analog-to-Digital conversion
The sensor measures the exposure signal at each R,G,B pixel.
This signal must be digitized : quantized and then coded in binary.
To have proper exposure, before digitization, some cameras perform:
“gain control” – adjust overall sensitivity of responses
(this happens in photoreceptors of our eyes too)
“white balance” - adjust relative sensitivity of R,G,B
(e.g. if light source has dominant color)

## Slide 24
Gain control and white balancing

## Slide 25: RGB Histograms
“luminance” = .3 * R + .6 * G + .1 * B

## Slide 26: RAW image format
Some cameras allow you to save the captured digital values
(rather than coding using JPEG – see later).
The file format is called RAW. The details of the file format are not standard. Rather, they depend on the camera and they are proprietary.
https://en.wikipedia.org/wiki/Raw_image_format
Adobe Lightroom and Photoshop are an example of software that allows you read and manipulate RAW images, and save them in other formats such as JPG.

## Slide 27
ENCODER:
Camera (+ hardware/software)
converts to a standard format
RAW
image file
(12 bits per RGB value)
JPEG, TIFF, ….
image file

## Slide 28
ENCODER:
Camera (+ hardware/software)
converts to a standard format
RAW
image file
(12 bits per RGB value)
JPEG, TIFF, ….
(compressed image file)
Some formats are lossless.
Some are lossy.
Details omitted.
DECODER:
hardware/software
converts from a standard format to 8 bits per RGB
(sent to display)

## Slide 29
ENCODER:
Camera (+ hardware/software)
converts to a standard format
RAW
image file
(12 bits per RGB value)
JPEG, TIFF, ….
image file
?

## Slide 30: Demosaicing
Camera makers have invented lots of ways to demosaic in a smarter way than just interpolating values.
(12 bits per RGB value)

## Slide 31
Then what happens ?
How are the digitized (demosaiced) RGB values at each image position transformed?

## Slide 32
Recall the RGB spectral sensitivity depends on the camera.
This is a problem because the captured images will be displayed on devices that don’t know about that cameras.
Solution ?

## Slide 33: Color spaces
Recall the RGB spectral sensitivity depends on the camera.
This is a problem because the captured images will be displayed on devices that don’t know about that camera.
Solution:
Transform to a standardized color space e.g.
  RGB (camera specific) ⇒ “CIE XYZ” (1931)
  This transformation is a 3x3 matrix multiplication, which is camera dependent.

## Slide 34
color name purity intensity
(for HSV
color space)
Often transforms color again to separately encode different aspects of color.

## Slide 35
These three “perceptual dimensions” of color are non-linearly related to physical color. (Many details omitted !)
Color scientists have studied these non-linearities for decades, and we now have many powerful models and theories that are used in color industry (printing, displays, etc).
Here I give just a small taste….

## Slide 36
  RGB ⇒ CIE XYZ ⇒ CIE LAB
3x3 matrix multiplication
based on
non-linearities in
human visual perception
  HSV
  … and many more
  CIE LUV

## Slide 37
color name purity intensity
(for HSV
color space)

## Slide 38: RGB vs. HSL (similar to HSV)

## Slide 39: Example: Image compression standards (they encode HSV separately)
ENCODER:
(color transform,
compression)
RAW
image file
JPEG, TIFF, ….
image file
Both be either lossless or lossy.
DECODER:
(uncompress)

## Slide 40: Non-linearities in the display
If you send an R, G, B value to a display, the intensity of light emitted is
https://www.cambridgeincolour.com/tutorials/gamma-correction.htm

## Slide 41: sRGB: image standard for internet
ENCODER:
RAW
image file
sRGB
DECODER
(optional – values can be sent directly to display device !)
Relatively simple non-linear transform for R,G, B values
at each pixel (inverse gamma)
Non-linear
(gamma)

## Slide 42: Take home messages from today
RGB seems simple. But it’s not:
  RGB digital images typically have been encoded with a non-linear transform.
  When you manipulate RGB values in images, keep in back of your mind that they don’t represent what you think.